Pakin Panawattanakul
4 / Aug /2025

---
Presentation outline
Presentation outline
- Objective & Scope
- FPGAs used in implementation
- Accelerator architecture
- Future work

---
Objective & Scope
Objective & Scope
Optimize resource utilization for Kyber Accelerator
  - Reuse module for encryption and decryption
  - Use BRAM to store intermediate data
    - Between module
    - Pipeline
- Not include key-generation
- Aritmetic Pipeline in NTT and Hash Module

---
Notations
- Bit stream =
- Polynomial ring
lbrace {0,1} rbrace ^256
R_q

---
Modules sections
Control
Encapsulation
Decapsulation
Main computation
Note Computations module are shared between Encapsulation and Decapsulation
`

---
Encapsulation process
Encapsulation
Module &
Dataflow

---
Pre/Post Indcpa Encryption
Pre-Encryption
Input
Public key:
R = Random 256 bits,
Output
m = SHA3-256(R) , Plain text message
ρ={0,1}^256 , hat t = left( stack{R_q # R_q # R_q} right) newline
(ρ,hat t)
R= lbrace 0,1 rbrace^256
(coins,pre-k^,)=SHA3-512(SHA3-256(PK),m)
m,coins,pre-k^, = {0,1}^256

---
Decode PK
Decode PK
Split public key into two part
Input : public keys
Output
Seed = ρ
Increase coef size 12→16bits
PK = (ρ,hat t)
hat t
t
ρ= lbrace 0,1 rbrace^256, hat t = left ( stack{R_q # R_q # R_q} right )

---
Decode Msg
Input : m plain text = )
Calculate
For every bit covert: 0 → 0, 1 → 1665
Output : (polynomial form )
lbrace 0,1 rbrace^256
q=3329
m_{poly} = rounded(q/2)m=1665m
m_{poly}
R_q
color red m_poly

---
Hash Sampling Rejections
Hash Sampling Rejections
Input
Seed =
Coins =
Output : small polynomial errors &
Part of public keys
lbrace 0,1 rbrace^256 newline lbrace 0,1 rbrace^256
color red {size 14 {r}}
color red hat A ^T
e_1 newline e_2 newline r newline {hat A}^T
r = left( stack{S_η # S_η # S_η } right)," " e_1 = left( stack{S_η # S_η # S_η} right), " "e_2 = S_η
color red {size 14 {e_1,e_2}}
{hat A}^T = left( stack{Z[x] # Z[x] # Z[x]}" " stack{Z[x]# Z[x]# Z[x]} " "stack{Z[x]# Z[x]# Z[x]} right)

---
NTT Module
Convert polynomial to NTT form
Input : small polynomial
Output : polynomial in NTT, Polynomial Ring form
r = left(stack{S_η #S_η #S_η} right)
color red { hat r}
hat r = left(stack{R_q # R_q # R_q} right)
hat r = NTT(r)

---
PACC : Polynomial Accumulator
PACC : Polynomial Accumulator
Compute polynomial aritmetic in NTT form with mondgomery multiplications
Input : Error Polynomial, variable from PK
hat r
hat t = left ( stack{R_q # R_q # R_q} right )
hat r = left(stack{R_q # R_q # R_q} right)
{hat A}^T = left( stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} right)
{hat A}^T
hat t
color red{hat u, hat x}
Output
Note is only intermediate value before computation of
hat x = {hat A}^T hat r newline hat y = {hat t}^T hat r
hat x, hat y
hat u,hat v

---
INTT Module
Convert Polynomial in NTT back to normal form
Input :
Output
hat x = left(stack{R_q # R_q # R_q} right) ," "hat y= R_q
hat x, hat y
x = left(stack{R_q # R_q # R_q} right) ," "y= R_q
x = NTT^{-1}(hat x)newline y = NTT^{-1}(hat y)
color red{u,x}

---
Addition Module (+)
Compute polynomial addition
Input
x = left(stack{R_q # R_q # R_q} right) ", " y= R_q
x,y
m_poly
e_1=left( stack{S_η#S_η#S_η}right)", "e_2 = S_η
e_1,e_2
m_{poly}=R_q
Output
u = x +e_1
u = left(stack{R_q # R_q # R_q} right) ", " v= R_q
v = y +e_2+m_poly
color red{u,v}

---
Reduce Module
Mondgomery reduction reduce the coefficient to be with in [0,q)
Input : polynomials
v
u
u = left(stack{P # P # P} right) ", " v= P
Output : polynomials ring
u
v
R_q
u = left(stack{R_q # R_q # R_q} right) ", " v= R_q
color red{u,v}

---
Compress encode
Compress ciphertext using rounded funciton
Input : u,v
Compute
color red{u,x}
c_1 = compress(u,d_u)=round((2^d/q)x)mod 2^d newline c_2 = compress(v,d_v)=round((2^d/q)x)mod 2^d
Output
      Cipher text
Ct = (c_1,c_2)

---
Post Indcpa Encryption
Input
Ct : cipher text
Pre–k^,
Output
Ct : cipher text
Ss = SHAKE-256(SHA3-256(Ct),	)
Pre-k^,

---
Decapsulation
Module & Dataflow

---
Pre Indcpa Decryption
Recive and pass input to other module as it is
Input
Cipher text :
Private key :
Ct = (c_1,c_2)
SK = (hat s, PK,pre-k,coin)
Output:
Cipher text :
Private key :
Ct = (c_1,c_2)
SK = (hat s, PK,pre-k,coin)

---
Decode Ct
Recive and pass input to other module
Input : Cipher text
Output:
color red {u^'}
Ct = (c_1,c_2)
u^' = decompress(c_1,d_u)=round((q/2^d)c_1)mod q newline v^' = decompress(c_2,d_u)=round((q/2^d) c_2)mod q
color red {v^'}

---
Decode SK
Decode Encapsulation key then Transpose encryption key
Input : Private key
Output : encryption key
color red{{hat s}^T}
SK = (hat s, PK,pre-k,coin)
{hat s}^T

---
NTT module
Convert polynomial to NTT
Input : Part of cipher text
Output : cipher text in NTT form
u'
color red{{hat u'}}
{hat u'} = NTT({u'})

---
PACC : Polynomial Accumulator
Compute polynomial aritmetic in NTT form with mondgomery multiplications
Input
Part of cipher text :
Encryptions key (transposed) :
Output : intermidiate data
hat {u'}
color red{{hat a}}
{hat s}^T
hat a = {hat s}^T times hat u'

---
INTT module
Inverse polynomial in NTT to normal form
Input : intermediate data (NTT form)
Output : intermidiate data (normal form)
hat a
a = NTT^-1(hat a)
color red{{a}}

---
Subtraction Module (-)
Subtract
Input : intermediate data (NTT form)
Output : intermidiate data (normal form)
hat a
a = NTT^-1(hat a)
color red{{a}}

---
Dual port BRAM
Dual port BRAM

---
Reference to Kyber Algorithm
Reference to Kyber Algorithm
https://cryptography101.ca/kyber-dilithium/

---
Kyber PKE
Kyber PKE

---
Kyber KEM
Kyber KEM