Pakin Panawattanakul
4 / Aug /2025

---
Presentation outline
Presentation outline
- Objective & Scope
- FPGAs used in implementations
- Accelerator architecture
- Result
- Future work

---
Today presentation
Today presentation
- Literature review of pure hardware implementation
- Implements Architecture and modules
- Encapsulations and Decapsulation dataflow
- Adaptation to our project

---
Objective & Scope
Objective & Scope
Optimize resource utilization
  - Reuse module for encryption and decryption
  - Use BRAM to store intermediate data
    - Between module
    - Pipeline
- Not include key-generation
- Aritmetic Pipeline in NTT and Hash Module

---
Modules sections
Control
Encapsulation
Decapsulation
Main computation
Note Computations module are shared between Encapsulation and Decapsulation
`

---
Flow charts of Kyber

---
Encapsulation process
Encapsulation
Module &
Dataflow

---
Pre/Post Indcpa Encryption
Pre-Encryption
Input
Public key:
R = Random 256 bits,
Output
m = SHA3-256(R) , Plain text message
ρ={0,1}^256 , hat t = left( stack{R_q # R_q # R_q} right) newline
(ρ,hat t)
R= lbrace 0,1 rbrace^256
(coins,pre-k^,)=SHA3-512(SHA3-256(PK),m)
m,coins,pre-k^, = {0,1}^256

---
Decode PK
Decode PK
Split public key into two part
Input :
Output
Seed = ρ
Increase coef size 12→16bits
PK = (ρ,hat t)
hat t
t
ρ= lbrace 0,1 rbrace^256, hat t = left ( stack{R_q # R_q # R_q} right )

---
Decode Msg
Input : m plain text = )
Calculate
For every bit covert: 0 → 0, 1 → 1665
Output : (polynomial form )
lbrace 0,1 rbrace^256
q=3329
m_{poly} = rounded(q/2)m=1665m
m_{poly}
R_q
color red m_poly

---
Hash Sampling Rejections
Hash Sampling Rejections
Input
Seed =
Coins =
Output : small polynomial errors &
Part of public keys
lbrace 0,1 rbrace^256 newline lbrace 0,1 rbrace^256
color red {size 14 {r}}
color red hat A ^T
e_1 newline e_2 newline r newline {hat A}^T
r = left( stack{S_q # S_q # S_q } right)," " e_1 = left( stack{S_q # S_q # S_q } right), " "e_2 = S_q
color red {size 14 {e_1,e_2}}
{hat A}^T = left( stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} right)

---
NTT Module
Convert polynomial to NTT form
Input : small polynomial
Output :
polynomial in NTT form
r = left(stack{R_q # R_q # R_q} right)
color red { hat r}
hat r = NTT(r)
hat r = left(stack{R_q # R_q # R_q} right)

---
PACC : Polynomial Accumulator
PACC : Polynomial Accumulator
Compute polynomial aritmetic in NTT form with mondgomery multiplications
Input : Error Polynomial, variable from PK
hat r
hat t = left ( stack{R_q # R_q # R_q} right )
hat r = left(stack{R_q # R_q # R_q} right)
{hat A}^T = left( stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} stack{R_q # R_q # R_q} right)
{hat A}^T
hat t
color red{hat u, hat x}
Output
Note is only intermediate value before computation of
hat x = {hat A}^T hat r newline hat y = {hat t}^T hat r
hat x, hat y
hat u,hat v

---
INTT Module
Convert Polynomial in NTT back to normal form
Input :
Output
hat x = left(stack{R_q # R_q # R_q} right) ," "hat y= R_q
hat x, hat y
x = left(stack{R_q # R_q # R_q} right) ," "y= R_q
x = NTT^{-1}(hat x)newline y = NTT^{-1}(hat y)
color red{u,x}

---
Addition Module (+)
Input
x = left(stack{R_q # R_q # R_q} right) ", " y= R_q
x,y
m_poly
e_1=left( stack{R_q# R_q# R_q}right)", "e_2 = R_q
e_1,e_2
m_{poly}=R_q
Output
u = left(stack{R_q # R_q # R_q} right) ", " v= R_q
u = x +e_1
v = y +e_2+m_poly
color red{u,v}

---
Compress encode
Compress ciphertext using rounded funciton
Input : u,v
Compute
color red{u,x}
c_1 = compress(u,d_u)newline c_2 = compress(v,d_v)
Output
      Cipher text
Ct = (c_1,c_2)

---
Post Indcpa Encryption
Input
Ct : cipher text
Pre–k^,
Output
Ct : cipher text
Ss = SHAKE-256(SHA3-256(Ct),	)
Pre-k^,

---
Decapsulation
Module & Dataflow

---
Dual port BRAM
Dual port BRAM

---
Reference to Kyber Algorithm
Reference to Kyber Algorithm
https://cryptography101.ca/kyber-dilithium/

---
Kyber PKE
Kyber PKE

---
Kyber KEM
Kyber KEM